16E1 Fiber Optical Multiplexer

User’s Reference Manual

To Users：

Thank you for using our products. Before using, please read this Reference Manual carefully, and keep properly.

Alarm

1、This product can not be caught in or be affected with damp, for they can make the performance degressive and even broken

2、Before fixing this product ,please check the model and according to the User’s Reference Manual.

Contents

1 Product Description	1

1.1 Function Description	1

1.2 Features	1

1.3 Application	2

1.4 Specification	3

2 Installation	5

2.1 Site Selection	5

2.2 Mechanical Installation	5

2.2.1 RS232 interface（optional component）	6

2.2.2 Indicator light	6

2.2.3 Front panel DIP definition	7

2.2.4 Front panel PUSH button definition:	9

2.2.5 Hot line phone (optional component)	9

2.2.6 Ethernet (optional component)	10

2.2.7 Rear Panel	11

2.2.8 Power supply	12

3 Operation	14

3.1 Equipment installation	14

3.1.1 Quick installation	14

3.1.2 Cautions about installation	15

3.2 Power on the equipment	16

3.3 Troubleshooting	17

4. Packing	18

4.1 packing pattern	18

# 1 Product Description

## 1.1 Function Description

16E1 Fiber Optical Multiplexer can multiplex to 16 E1 signals for transmission over an optical fiber, resulting in reaching a longer distance without a repeaters and superior performance compared to copper media.

16E1 Fiber Optical Multiplexer is the 16E1 point-to-point optical transport equipment that uses the FPGA chips and it is easy to upgrade. It is single board structure and the largest transmission capacity is 16E1. The outer design use the standard 19 inches rack, so the volume is little, weight is light and operation is convenient and credit.

16E1 Fiber Optical Multiplexer , adopts the PDH fiber transmission technologies. The 2M (E1) interfaces can connect with the exchanger, light loop device and multi-diplexer directly to form the mircomidi or the special network. Complete alarm function for 16E1 Fiber Optical Multiplexer, it is stable and easy to maintenance, install and small in size. It has one digital service telephone.

## 1.2 Features

The features for 16E1 fiber Multiplexer list below:

- Offer 16 × 2Mb/s digital interfaces

- Up to 16 E1 links on one fiber

- One link to service telephone for duty contract

- 180-260VAC & -48VDC power options and the positive and negative of DC-48V can be optional because there is the self-test circuit for the polarity inside th1e device

- Standard 19 inches rack, little volume, light weight, steady capacity and convenient setup

- Digital clock recovery circuit and digital smooth DPLL adopted for 2.048Mb/s port

- LED indicators

- Phone Hotline

- Ethernet interface

## 1.3 Application

16E1 Fiber Optical Multiplexer can be used a high-speed baseband modem for point to point that connects two DTE over a lease Line. From Router ( CSU/DSU ( 16E1 Fiber Optical Multiplexer ( Optical Fiber( 16E1 Fiber Optical Multiplexer ( CSU/DSU( DTE as illustrated in the Following Diagram.

Diagram 1.1

## 1.4 Specification

E1 line Interface

Optical Fiber Interface

Note: Longer or shorter distance 50km or above (120km) , on special order

Physical/Electrical

Timing

- Timing derived from incoming E1

Diagnostics Test

- Loop-back testing for 16 × E1 (Local and remote)

- Loop-back testing for fiber optical (Local and Remote)

Indicators

- Local optical signal indications for all E1s.

- Remote optical signal receive indication, working and loss.

- Loop-back indication.

- Alarm indication, on or off.

- Power on indication.

# 2 Installation

## 2.1 Site Selection

This is a guideline for 16E1 Fiber Optical Multiplexer installation. The following list indicates a site selection guideline. User needs to follow this guideline for the select a proper installation site.

- For the 16E1 Fiber Optical Multiplexer unit, the location should be part of the Central Office (CO) equipment layout design. The entrance cable routing should be consider.

- The installation should provide a proper room for the adequate ventilation and cable routing at site. At least 0.5 m should be reserve at the rear of the unit for the human access, cable, and airflow.

- The site should provide a stable environment. The Ops Area (Operating Area) should be free from extremes temperature, humidity, shock and vibration.

- Do not expose the unit under the rain cause 16E1 Fiber Optical Multiplexer wasn’t a waterproof unit.

- Relative humidity should stay between 0 and 95%.

- Survey the site (power supply) before install the unit.

## 2.2 Mechanical Installation

16E1 Fiber Optical Multiplexer is a desktop and rack mount unit, which offers two kinds of power supply AC or DC.

The front panel is shown below:

Front Panel

### 2.2.1 RS232 interface（optional component）

the equipment supply one channel of RS232 interface ,  pins are as follows：

| pin | definition | description |
| --- | --- | --- |
| 2 | TXD | output |
| 3 | RXD | input |
| 5 | GND | Ground |

### 2.2.2 Indicator light

Table 2.2.1

| No. | Name | Color | Status | Describe |
| --- | --- | --- | --- | --- |
| 1 | LOS1 | Red | Active | E1 port 1 loss |
| 2 | LOS2 | Red | Active | E1 port 2 loss |
| 3 | LOS3 | Red | Active | E1 port 3 loss |
| 4 | LOS4 | Red | Active | E1 port 4 loss |
| 5 | LOS5 | Red | Active | E1 port 5 loss |
| 6 | LOS6 | Red | Active | E1 port 6 loss |
| 7 | LOS7 | Red | Active | E1 port 7 loss |
| 8 | LOS8 | Red | Active | E1 port 8 loss |
| 9 | LOS9 | Red | Active | E1 port 9 loss |
| 10 | LOS10 | Red | Active | E1 port 10 loss |
| 11 | LOS11 | Red | Active | E1 port 11 loss |
| 12 | LOS12 | Red | Active | E1 port 12 loss |
| 13 | LOS13 | Red | Active | E1 port 13 loss |
| 14 | LOS14 | Red | Active | E1 port 14 loss |
| 15 | LOS15 | Red | Active | E1 port 15 loss |
| 16 | LOS16 | Red | Active | E1 port 16 loss |
| 17 | OLOS | Red | Active | Optical Signal lost |
| 18 | OLOF | Red | Active | Optical SYNC loss |
| 19 | E3 | Red | Active | Optical BER≥10-3 |
| 20 | F2 | Green | Active | Spare fiber work on second channel |
| 21 | LINK | Green | Active | LAN Link and Active |
| 22 | SPD | Green | Active | On:100M,OFF:10M |
| 23 | PWR | Green | Active | Power on |

### 2.2.3 Front panel DIP definition

On the front panel of standalone definition as follows:

When MSK button push up, ( RLOOP1-16 ): 1-16 E1 remote loop. If the RLOOP1 is ON，this means that at the far end it is doing a E1 loop-back.

0 means ON,1 means OFF

Table 2.2.2

When MSK button push down, Bit1-5(mask1-5):1-16 E1 warning shielding.

1 means off, 0 means on

Bit 6-8: reserved

### 2.2.4 Front panel PUSH button definition:

In the front panel ,there are four push button ,It is MSK, SMSK, LRS, PH

The function described following table 2.2.3

| PUSH | OFF | ON |
| --- | --- | --- |
| MSK | DIP1-5 be used E1 warning shield | DIP1-5 be used E1 remote loop |
| SMSK | (standalone) warning voice is on | (standalone) warning voice is off |
| LRS | LED means Local | LED means Remote |
| PH | Hot line phone not used | Use Hot line phone |

Table 2.2.3

In table 2.2.3 OFF means Push button UP,ON means push button Down.

### 2.2.5 Hot line phone (optional component)

Hot line phone, not occupy 2M channel transmission.

On the front panel there is a “PH” button, press on the “PH” button on the remote site it will sound.

To answer it the remote site just need to press the “PH” button on the remote unit, the alarm will cut off and just plug in the phone both side able to do the communication.

Setting of the manage phone:

- It does not occupy the 2M circuits.

### 2.2.6 Ethernet (optional component)

16E1 Fiber Optical Multiplexer can offer a channel for 10/100M ,full/duplex auto-negotiation LAN interface, support VLAN protocol, this interface can continuous learn MAC addresses in the LAN that connected with it, and send the address as frame in another LAN. Transparence to TCP/IP protocol, offers security connection between different equipments in the network, used widely in network connection and monitor between WAN and LAN.

- 10/100 Base-T Ethernet port parameter

- Rate: 10M or 100M, full/semi duplex auto-negotiation

- Ethernet rate in optical line: 100M.

- Protocol: support IEEE 802.3, IEEE 802.1Q(VLAN)

- MAC address table: can learn 4096 MAC address

- Ethernet buffer memory: 64 Mbits SDRAM

- Physical interface: RJ45 slot, support AUTO-MDIX

Ethernet operating diagram:

Ethernet RJ45 ports connection:

### 2.2.7 Rear Panel

Table 2.2.6 describe the rear panel interface.

Table 2.2.6

| Interface | Describe |
| --- | --- |
| AC220V | 220V AC Power Adapter |
| DC-48V | DC(-36 to 72V)In no use |
| TX | Fiber TX out |
| RX | Fiber RX In |
| OUT1 | Port1 E1 Transmit (75Ω unbalance) |
| OUT 2 | Port2 E1 Transmit (75Ω unbalance) |
| OUT 3 | Port3 E1 Transmit (75Ω unbalance) |
| OUT 4 | Port4 E1 Transmit (75Ω unbalance) |
| OUT 5 | Port5 E1 Transmit (75Ω unbalance) |
| OUT 6 | Port6 E1 Transmit (75Ω unbalance) |
| OUT 7 | Port7 E1 Transmit (75Ω unbalance) |
| OUT 8 | Port8 E1 Transmit (75Ω unbalance) |
| OUT 9 | Port9 E1 Transmit (75Ω unbalance) |
| OUT 10 | Port10 E1 Transmit (75Ω unbalance) |
| OUT 11 | Port11 E1 Transmit (75Ω unbalance) |
| OUT 12 | Port12 E1 Transmit (75Ω unbalance) |
| OUT 13 | Port13 E1 Transmit (75Ω unbalance) |
| OUT 14 | Port14 E1 Transmit (75Ω unbalance) |
| OUT 15 | Port15 E1 Transmit (75Ω unbalance) |
| OUT 16 | Port16 E1 Transmit (75Ω unbalance) |
| IN1 | Port1 E1 Receive (75Ω unbalance) |
| IN2 | Port2 E1 Receive (75Ω unbalance) |
| IN3 | Port3 E1 Receive (75Ω unbalance) |
| IN4 | Port4 E1 Receive (75Ω unbalance) |
| IN5 | Port5 E1 Receive (75Ω unbalance) |
| IN6 | Port6 E1 Receive (75Ω unbalance) |
| IN7 | Port7 E1 Receive (75Ω unbalance) |
| IN8 | Port8 E1 Receive (75Ω unbalance) |
| IN9 | Port9 E1 Receive (75Ω unbalance) |
| IN10 | Port10 E1 Receive (75Ω unbalance) |
| IN11 | Port11 E1 Receive (75Ω unbalance) |
| IN12 | Port12 E1 Receive (75Ω unbalance) |
| IN13 | Port13 E1 Receive (75Ω unbalance) |
| IN14 | Port14 E1 Receive (75Ω unbalance) |
| IN15 | Port15 E1 Receive (75Ω unbalance) |
| IN16 | Port16 E1 Receive (75Ω unbalance) |

### 2.2.8 Power supply

16E1 Fiber Optical Multiplexer support 3 type powers: AC220V, -48V and +24V.

If the power of DC-48V is used, the positive and negative terminal can be optional because there is the self-test circuit for the polarity inside the fiber optical Multiplexer

Note: This device offers AC220V power supply.

# 3 Operation

## 3.1 Equipment installation

After unpacking and before installation, make sure checking the following:

- Make sure the package is well. If the package is damaged, contact our service office quickly for solution.

- Check the package according to the product list, if find equipment severe damaged or lack of some components, please contact the installation workers or our service office.

- Check whether the equipment type is meet with the type you ordered.

- Check whether the component is integrity.

- Check the power supply type.

# 3.1.1 Quick installation

- Fasten the Equipment in 19 inch. rack with the screws in the equipment package.

- Use reliable ground connection at GND point of the equipment

- Use power tab to connect power according to the manual, don’t exchange the polarities.

- Create user equipment connecting wire according to your demand (2M, V.35 and 10 Base-T), then connected, don’t exchange receive and transfer wires.

- Connect receive and transfer optical with optical receive and transfer port of the equipment. Don’t exchange receive and transfer wire, make sure the optical fiber head is clean, insert optical jumper, make sure connection well. (fiber bending radius≥50 mm)

- Use multimeter to test power polarity and voltage, make sure it match with equipment requirement.

- After complete installation and make sure it’s ok, power on the switch. Check indicator light meet with practice situation (see related part of manual).

- A clean, steady environment and firm installation should provided for independent or wall hanging equipment.

# 3.1.2 Cautions about installation

- Avoid severe libration and mechanical damage during the process of transfer and installation.

- Arrange fiber appropriately, fiber bending radius≥50 mm.

- Check voltage and polarity meet with back panel, or it will cause permanent damage to the equipment.

- Fiber connector can’t contaminate, wipe optical fiber head slightly using alcohol, or it will affect transmission. If the fiber connector not butt joint well, it may be cause power decline, adjust fiber connector according to practical situation.

- The installation position should convenience for personal pass and equipment movement.

- The environment should dry, clean and ventilation well.

- Essential static-protective is needed during the installation and maintenance, ground the chassis to increase anti-interference capability and prevent lightning strike. Before use the equipment, independence work ground and protect ground should provided, make sure it ground well.

## 3.2 Power on the equipment

- Check indicators and alarms according to manual after power on.

- If both local and remote work well, fiber interface connect ok, the alarm light OPLOS and OPLOF off, POWER indicator light is green.

- Light LOSX (X=1-16) is red and voice alarm is on because of not connecting E1 signal. After connect E1 signal, light LOSX (X=1-16) will off, voice alarm will off until all light LOSX is off.

- Branch shield: shield no using branch alarm, no red light is on when all alarm is off.

- Hot line phone: after Optical Multiplexer works normally, insert microphone to hot line phone port, press button PHONE to call remote user, then can communication after the remote user press button PHONE and hold up the microphone. Buzzer rings when remote terminal call local terminal, press button PHONE and hold up microphone, then communicate with remote terminal. Back the button PHONE to norm after communication is completed.

- Branch loop: when system work normally and no branch alarm happen, loop test is available with SW. put the SW switch to ON in local terminal, can control remote corresponding 2 Mb/s branch to loop, then can test corresponding output signal at local 2 Mb/s output port. Use this function you can realize loop of all the branches, and it’s easy for detect.

- Use bit error instrument to analyzing performance of 2M branch, and record it.

- Close voice alarm: voice alarm on when following situation happened:

A. Optical disconnected cause OPLOS alarm.

B. Signal not steady cause OPLOF alarm.

C. Some branches not use and not shielded.

Push down SW5 at local terminal, can control closing voice alarm.

Note: after failure is removed, set the button to norm, validate the alarm function

## 3.3 Troubleshooting

Best status is configured to this equipment before out of factory. All the functional interfaces are at the front and back panel. Please don’t open the chassis yourself. If have failure, you can determine the range of failure using single loop, and contact our corporation.

The following table list common failure and alarm, the reason may cause these alarm and solution to this alarm for you to reference.

Equipment alarm and corresponding solution

Table 3.3

# 4. Packing

## 4.1 packing pattern

Following are in the 16E1 Fiber Optical Multiplexer Package:

16E1 Fiber Optical Multiplexer ----------------------------	1

220AC Power Supply wire----------------------------------	1

Users manual--------------------------------------------------	1

Mircophone---------------------------------------------------    1

BNC ------------------------------------------------------------	16

NOTE：

- 16E1 Fiber Optical Multiplexer is a sensitive electronic item, please do handle with extra care during delivery or shifting.

- This unit will be warranty for 1 year.

- Within the warranty period, whenever there is a problem regarding the quality issue, We will take the responsibility to repair with free.

- After the warranty period, we will charge accordingly depend on the fault or damage.

- Whenever there is a fault, try to identify the problem and the alarm. Of course, you can contact our technical support at any time.